## Slide 1: Rapid-deployment aortic valves for patients with a small aortic root: A single‑center experience
Coti L et al. The Annals of Thoracic Surgery. 2020. doi:10.1016/j.athoracsur.2020.02.030.

## Slide 2: Study details
Aim: To assess PPM incidence and haemodynamic performance in patients with a small aortic root, and the impact on early- and intermediate-term mortality, following implantation with the EDWARDS INTUITY valve (19- and 21- mm)
Study type: Cohort analysis
Primary endpoints: Mortality rates, haemodynamic performance, PPM incidence, valve-related events and NYHA functional class
Methods:
  659 patients with severe AS underwent AVR with an EDWARDS INTUITY valve between May 2010 and November 2018
  Data from 32.9% patients who received a 19- or 21-mm bioprostheses were analysed

## Slide 3: Key study results (1/4)
Patient characteristics
  A total of 217 patients received a 19- or 21-mm EDWARDS INTUITY valve
  Dyslipidaemia was the most common comorbidity (59%)
  Mean follow-up was 24 ± 23 months

## Slide 4: Key study results (2/4)
Procedural characteristics
  40.6% patients underwent concomitant procedures, with CABG being the most common (23%)
  Mean CPB time for isolated AVR was 101.1 ± 31.9 minutes
  Mean cross-clamp time for isolated AVR was 67.2 ± 23.2 minutes
  Mean overall CPB and cross-clamp times were 117.8 ± 49.4 minutes and 79.8 ± 36.3 minutes
Mortality
  Mortality rate: 12.4%; 1.8% perioperatively, and 0.5% during the first month
  Survival not significantly influenced by degree of PPM (HR: 0.95; 95% CI 0.75 to 1.19: p=0.638)

## Slide 5: Key study results (3/4)
Clinical outcomes
  NYHA functional scores: 1.5 ± 0.7 versus 2.8 ± 0.6 (preoperative)
  PPM: 35.5% of patients (25.8% moderate and 9.7% severe):
    19 mm valve: 33% (moderate) and 10% (severe)
    21 mm valve: 23% (moderate) and 9% (severe)
    Body surface area and mean gradient higher in patients with PPM than those with no PPM
  Pacemaker implantation rate: 11.5%
  Reoperation rate: 2.3%

## Slide 6: Key study results (4/4)
Haemodynamic outcomes
  Mean gradients reduced between discharge and 5-year follow-up:
    19 mm valve: 17.8 ± 6.3 mmHg (mean) and 32.7 ± 11.8 mmHg (peak)
    21 mm valve: 13.5 ± 4.7 mmHg (mean) and 23.9 ± 7.2 mmHg (peak)
  EOA and iEOA were 1.55 ± 0.36 cm2 and 0.87 ± 0.22 cm2/m2:
    19 mm valve: 1.44 ± 0.37 cm2 and 0.83 ± 0.26 cm2/m2
    21 mm valve: 1.59 ± 0.35 cm2 and 0.89 ± 0.21 cm2/m2
Mean Gradients

## Slide 7: Study limitations and conclusion
Limitations
  Potential lack of a homogenous sample due to varied inclusion criteria
Conclusion
The EDWARDS INTUITY valve demonstrated excellent haemodynamic performance and early and intermediate term survival rates, functional class improvements and a reduced PPM incidence. Rapid deployment AVR might be a superior solution to be considered in patients with small aortic annulus.

## Slide 8
This document is a summary of the Coti L et al. paper and covers key information including aim, type of study, methods, results, limitations and conclusions.
The full publication is available at: https://bit.ly/2xyQ8YU
Abbreviations
AS: Aortic stenosis iEOA: Indexed effective orifice area
AVR: Aortic valve replacement NYHA: New York Heart Association
CABG: Coronary artery bypass graft PPM: Patient–prosthesis mismatch
CI: Confidence interval SAVR: Surgical aortic valve replacement
CPB: cardiopulmonary bypass SD: Standard deviation
EOA: Effective orifice area STS: Society of Thoracic Surgeons
EuroSCORE II: European System for Cardiac Operative Risk Evaluation II score TAVR: Transcatheter aortic valve replacement
HR: Hazard ratio
Important safety information:
Use of the EDWARDS INTUITY Elite valve system may be associated with new or worsened conduction disturbances, which may require a permanent cardiac pacemaker implant (PPI). The rate of PPI for the EDWARDS INTUITY Elite valve is within the range reported in the literature for various rapid deployment valves, but higher than that reported for surgical aortic valves. Physicians should assess the benefits and risks of the EDWARDS INTUITY Elite valve prior to implantation. See instructions for use for additional information.
For professional use. For a listing of indications, contraindications, precautions, warnings, and potential adverse events, please refer to the Instructions for Use (consult eifu.edwards.com where applicable).
Edwards devices placed on the European market meeting the essential requirements referred to in Article 3 of the Medical Device Directive 93/42/EEC bear the CE marking of conformity.
Edwards, Edwards Lifesciences, the stylized E logo, EDWARDS INTUITY, and EDWARDS INTUITY Elite are trademarks or service marks of Edwards Lifesciences Corporation or its affiliates. All other trademarks are the property of their respective owners.
© 2020 Edwards Lifesciences Corporation. All rights reserved. PP--EU-0171 v1.0